2. Descriptions of highlighted blocks.

ADJ11 – This block performs a 1-bit shift and sign extension on the offset11 bits from the instruction (IR[10:0]). This block is used by the JSR instruction.

PC_ADDER – This block performs addition on the PC and the sign extended offset passed to it. This block is used by BR, JSR, and LEA.

ZEXT8<<1 – This block performs a 1-bit shift and zero-extension on the trap vector (IR[7:0]). This block is used by TRAP.

Copy low to high – This block passes sr1 from the register file to the mdrmux. This block is used by STB.

SEXT5 – This block performs sign extension on the imm5 output from the IR. This block is used by AND and ADD.

SEXT6 – This block performs sign extension on the offset6 output from the IR. This block is used by LDB.

ZEXT4 – This block performs zero-extension on the imm4 output from the IR. This block is used by SHF.

ZEXT8 – This block performs zero-extension on the low or high byte from mem_wdata. This block is used by the LDB instruction.